## Slide 1: Fundamentals of Hardwired control
  In the past, hardwired control unit was very difficult to design as its engineering cost is very high.
  Presently, the emphasis of computer design is on the performance, therefore hardwired control is chosen.

## Slide 2: Fundamentals of Hardwired control
  controller of a hardwired control unit is viewed as a sequential logic circuit that implements microoperations using a combinational circuit.
  The inputs are from the microperation counter, instruction register and status register, which are transformed into a set of outputs that are the control signals.

## Slide 3: Hardwired Processor
Instruction Decoder
Encoder/Decoder
Inputs from system bus
Status and Condition Flags
I1
I2
In
Control Signals
Control step counter
Clock
IR

## Slide 4: Hardwired Processor
  The control unit gets opcodes from the instructions and will perform different actions based on the combinations of control signals.
  Starting with description of the behavior of the control unit, state diagram of micro-operations is constructed.
  From state diagram, hardware realization can be constructed.

## Slide 5
This concept can be explained by taking an example.
Some common statements of a program are described in Figure 4.3:

## Slide 6
:LOOP: if COND 1 = true then ADD A,B Else MUL A,B; if COND 2 = true then go to OUTPUT Else LOOP; OUTPUT
Figure 4.3 Example statements in a program

## Slide 7
Current State | Current Input | Next State | Current Outputs Function Storage | 
ADR1 ADR1 ADR2 ADR2 | COND1 = 1 COND1 = 0 COND2 = 1 COND2 = 0 | ADR2 ADR2 ADR3 ADR1 | ADD … MUL … … … … … | 
The state-table format for the above statements is shown in Figure 4.4
TABLE 2
Figure 4.4 State-Table format of statements of Figure 4.3
m

## Slide 8: Designing Hardwired Control Unit
  From state table, hardware realization can be constructed.
  Any sequential circuit, which can implement a state machine, can be constructed from combination circuit with feedback

## Slide 9: design Processor computing Greatest Common Divisor (GCD)
To find GCD of two numbers X and Y,
the smaller of the two numbers is subtracted from the bigger one.
process is repeated until we obtain the number that divides the other.
The procedure to perform the GCD is described in Figure 4.5.

## Slide 10
GCD(in: X,Y; out: Z);
Register XR, YR, TEMPR;
XR:=X; {Input data}
YR:=Y;
While XR>0 do begin
If XR YR then begin {Swap XR and YR)
TEMPR:=YR;
YR:=XR;
XR:=TEMPR; end
XR:=XR-YR {Subtract YR from XR}
End
Z:=YR (Output the result)
End. GCD;
Figure 4.5 State-Table format of statements of Figure 4.4
m

## Slide 11
state-table description of this algorithm is given in Figure 4.5, which gives the steps involved in finding the GCD of two numbers.
For example, with X=20 and Y=12, the GCD algorithm proceeds as in Figure 4.3.

## Slide 12
From the analysis of Figure 4.6, it can be judged that the datapath of this processor should have registers to store the variables XR and YR.
To perform subtraction and comparison, two functional units are needed.
To route the data on the relevant datapath at the appropriate time, a multiplexer is needed.
swap operation X:=Y, Y:=X can be done simultaneously in one clock cycle

## Slide 13
The inputs to the control unit are asynchronous reset signal, two comparison signals to compare if XR is equal to YR, or whether it is equal to YR (XRYR) and (XR>0), and the clock signal.
Control Signals needed by the control unit are Load, Select, Swap, Subtract.

## Slide 14: different states of the processor are defined based on the algorithm of the GCD
S0 = 00 begin
S1 = 01 swap
S2 = 10 subtract
S3 = 11 end

## Slide 15
TABLE 3 State Table for the GCD processor

## Slide 16
Using TABLE 3, an excitation-table is constructed listing the binary values of various variables at different times.
This is shown in TABLE 4.
Characteristic equation of D flip-flop is (t+1) = (t). Thus, for different values of D1 and D2, values of and can be defined. This excitation table is depicted in TABLE 4.

## Slide 17
S0 = 00, S1 = 01, S2 = 10 and S3 = 11

## Slide 20
(5.9)
(5.10)
(5.11)